## Slide 1: Coen 6501 Project
By
Group 5:
Chirag Jhamb
Yara Nouaiser
Yuvraj Prabhakar
Abdul Rahman Koleilat

## Slide 2: Design of ALU (8-bit)
Conversion of unsigned input operands to signed
Multiplier
Division by Four and Increment by One
Control Unit
Registers
Simulation
Synthesis

## Slide 4: Conversion of unsigned input operands to signed
2 Two’s complement generators are required.
All the input bits are inverted.
An incrementer will then add a 1.

## Slide 5: Multiplier
Algorithm
Partial Product Generator (PPG)
Adder

## Slide 6: Algorithm: Radix-4 Booth Multiplication
Extend the sign bit of the multiplier term so the number of bits are even.
A zero is appended to the right of the multiplier term.
Each 3-bit block of the multiplier will determine the operation performed on the multiplicand giving the partial product: Mx0, Mx1, Mx-1, Mx-2.
Multiplier Bits Block |  |  | Multiplier Value | Partial Product
Xi+1 | Xi | Xi-1 |  | 
0 | 0 | 0 | 0 | Mx0
0 | 0 | 1 | 1 | Mx1
0 | 1 | 0 | 1 | Mx1
0 | 1 | 1 | 2 | Mx2
1 | 0 | 0 | -2 | Mx-2
1 | 0 | 1 | -1 | Mx-1
1 | 1 | 0 | -1 | Mx-1
1 | 1 | 1 | 0 | Mx0

## Slide 7: Example
Consider "11100010" (-30) and "01110010" (114).
Going from right to the left, the 4 multiplier 3-bits are: 100, 001, 110, and 011.
Therefore, the four partial products will be:
  PP0: 0000000000111100
  PP1: 11111111100010
  PP2: 000000011110
  PP3: 1111000100
Adding the four partial products will give a sum of “1111001010100100” (-3420) which is correct.

## Slide 8: Partial Product Generator (PPG)
Decoder
Two’s Complement Generator
Shifter

## Slide 9: Decoder
The decoder will take the corresponding 3-bit multiplier block and give a 3-bit control signal.
The LSB will be the enable for the two’s complement generator.
The other 2 MSBs will be used for the shifter.
Multiplier Bits Block |  |  | Control Signal
Xi+1 | Xi | Xi-1 | 
0 | 0 | 0 | 000
0 | 0 | 1 | 010
0 | 1 | 0 | 010
0 | 1 | 1 | 100
1 | 0 | 0 | 101
1 | 0 | 1 | 011
1 | 1 | 0 | 011
1 | 1 | 1 | 000

## Slide 10: Two’s complement Generator
The multiplicand bits will be xored with the enable bit.
An incrementer will then add it with the enable bit.

## Slide 11: Shifter
The role of the shifter is to multiply the multiplicand by either 0, 1, or 2 depending on the first 2 bits of the control signal from the decoder.
It will either give a zero output, the multiplicand itself, or shift it to the left by 1 bit (x2).
When ctrl1 is 0, the output will be 0 if ctrl0 is 0 otherwise it’s the multiplicand itself (x1).
When ctrl1 is 1, the output will be the multiplicand shifted 1 bit to the left (x2).

## Slide 12: Adder
The adder is made up of 3 CLA’s to add the 4 partial products.

## Slide 13: Carry Look-Ahead Adder (CLA)
CLA is faster RCA since it computes the carry bits at the same time.

## Slide 14: Division by Four and Increment by One
Instead of using an incrementer, we could add 4 to the product of the multiplier by adding an input carry bit to the first CLA in the adder since the first two bits of the first partial product are not added. After that, shifting 2 bits to the right will give the final result.

## Slide 15: Control Unit
When the load signal transitions from 1 to 0, en1=1.
At the first rising edge of the clock, en1=0 and en2=1. End flag is 0.
At the second rising edge of the clock, both en1 and en2 are 0. End flag is 1.

## Slide 16: Registers
Two 8-bit registers are needed to latch the input operands A and B when en1=1.
One 16-bit register is needed to latch the output Z when en2=1.

## Slide 17: Simulation Result

## Slide 18: Area and Delay
 | LUTs | CLB Slices | Dffs or Latches
ALU with regular multiplier | 301 | 151 | 32
ALU with radix-2 booth multiplier | 348 | 174 | 32
ALU with radix-4 booth multiplier | 204 | 102 | 32
 | Delay
ALU with regular multiplier | 16.786 ns
ALU with radix-2 booth multiplier | 15.774 ns
ALU with radix-4 booth multiplier | 10.642 ns

## Slide 19: Expansion To 16 bits
Components are expanded to 16 bits.
8 PPG’s required.
The adder is made up of 7 CLA’s.

## Slide 20: Multiplier

## Slide 21: Adder

## Slide 22: Simulation Result

## Slide 23: Area and Delay
 | LUTs | CLB Slices | Dffs or Latches
8-bit ALU | 204 | 102 | 32
16-bit ALU | 886 | 443 | 64
 | Delay
8-bit ALU | 10.642 ns
16-bit ALU | 23.617 ns

## Slide 24: Pipelining of The Design
The original design uses 2 clock cycles for each operation.
The control unit needs to be modified and needs a counter.

## Slide 25: Simulation Result

## Slide 26: Area and Delay
 | LUTs | CLB Slices | Dffs or Latches
16-bit ALU | 886 | 443 | 64
16-bit ALU pipelined | 893 | 447 | 68
 | Delay
16-bit ALU | 23.617 ns
16-bit ALU pipelined | 23.617 ns

## Slide 27: Multiply Accumulate for Additional operands

## Slide 28: Simulation Result

## Slide 29: Area and Delay
 | LUTs | CLB Slices | Dffs or Latches
16-bit ALU | 886 | 443 | 64
16-bit ALU with Accumulator | 1043 | 522 | 109
 | Delay
16-bit ALU | 23.617 ns
16-bit ALU with Accumulator | 25.823 ns